## Slide 1: Xbee-Digimesh network
Presented By:
PRIYANSHU AJMERA
09/07/2018

## Slide 2: OUTLINE
Topologies in XBee
DigiMesh Network Setup
Wireless Data Transmission
XBee and Arduino Communication
DigiMesh Network
Routing

## Slide 3: Topologies in XBee
There are in total three topologies:
  Star Topology
  Tree Topology
  Mesh Topology

## Slide 4: DigiMesh network
A DigiMesh network is a topology in which we can use wireless end-point connectivity solutions. This can help us by providing various benefits such as: Self-healing, Routing, Peer-to-peer architecture, etc.
DigiMesh Network also supports multiple topologies like: Point-to-point, Point-to-multipoint and Mesh networks. Also, all the nodes are capable of Routing the data. Node can be a Coordinator, a Router or an End-Device
Indoor Range of XBee: Up to 2000ft (10kbps) & up to 1000ft (200kbps)
LOS Range of XBee: Up to 9 Miles (10kbps) & up to 4 Miles (200kbps)
No. of devices can connect at a time: Up to 128 nodes, but for larger networks up to 1000 nodes

## Slide 5: DigiMesh network
Benefits of DigiMesh Network:
  Routing: With this, the message is propagated through a path by hopping from one to other nodes until it reaches to the final destination
  Ad-hoc Network Creation: This helps in creating an automated network without any human intervention
  Self-healing: Even if any device gets disconnected, this process will redirect to the active node
  Peer-to-peer Architecture: No hierarchy or parent-child relationship is required
  Route Discovery: Instead of a particular map, the route is created on its own based on their discovery
  Reliable Delivery: Reliable data delivery is accomplished with the help of acknowledgements
  Quiet Protocol: Routing overhead is reduced by using a reactive protocol just like AODV (Ad-hoc On-Demand Distance Vector) Routing
Notes: AODV: It is a protocol which establishes an On-Demand route on a request of the source node.
The route will be established only till the time it is requested and the nodes not in the network will be silent without creating any extra traffic until a connection is established. Each nodes keep the track of the node requested to establish the connection so that a response message can be obtained from the same route.

## Slide 6: DigiMesh Network Setup
Before making a mesh network, we need to setup few values for every device in the network:
  Channel Mask (CM): 00FFFFFFFFFFF7FFFF
  Preamble ID (HP): 0 (Default)
  Network ID (ID): 2018
  Destination Address High (DH): 0
  Destination Address Low (DL): 0 (Unicast) or FFFF (Broadcast)
  Baud Rate (BD): 9600
  API Enable (AP): API Mode with Escapes(2)
  RSSI PWM Timer (RP): 5 (*100ms), by this we can set a timer for receiving a packet so that signal duty cycle gets updated and shuts off when the timer expires
  Node Identifier (NI): Name given to device for user understanding
  Routing/Message Mode (CE): Coordinator (Mode[1]), Router (Mode[0]), End-Device (Mode[2])

## Slide 7: DigiMesh Network Setup
UNICAST
Set 64 bit Address as the destination Address
BROADCAST
Set 64 bit Address as 000000000000FFFF

## Slide 8: DigiMesh Network Setup
BROADCAST TRANSMISSION:
  In Broadcast Transmission, the same data is transmitted to all the nodes present in the network
  This transmission goes throughout the network, so that data is received by all the nodes connected in the network
  To make this possible, all the receiving nodes and the starting node will transmit the data to the number of times mentioned by the Broadcast Multi-Transmit (MT) setting (the default value of MT is 3).

## Slide 9: DigiMesh Network Setup
UNICAST TRANSMISSION:
  In Unicast Transmission, the transmission of data to a single node in a network is identified by a unique 64-bit address
  The destination address can be an immediate neighbor or can be several hops away
  When DigiMesh unicast transmission, a reliable delivery of data can be accomplished with the help of reties and acknowledgements:
    For transmission between adjacent nodes, MAC retries/acknowledgement is used
    For an entire route, network retries/acknowledgement is used

## Slide 10: DigiMesh Network Setup
We can discover the devices in XCTU
Once we set all the parameters required to make them communicate, we can see the network in the Network Mode

## Slide 11: Wireless Data Transmission
Transmit Mode Sequence:
  If Route is known, the data packet is transmitted directly
  If Route is not known, movement to Route Discovery will happen so that we can establish a path to the destination node
  If no route is possible to reach the destination, the data packet is discarded and go back to Idle Mode
  Route discovery is done only once per packet

## Slide 12: Routing
Many a times, a direct Route is not possible because either they are placed very far apart from each other or the environment is making difficulty in connecting. To solve this, we use Bridge connection to make the communication possible
In bridge connection, the node is placed within the range of the starting node to pass the data, which then connected to another node to pass the data. This process continues until the data is reached to the final destination.
There are four types of Routing:
  Route Discovery
  Trace Routing
  Aggregate Routes
  Disable Routing

## Slide 13: Routing
Route Discovery
This process works on Ad-hoc On Demand Distance Vector Routing (AODV) protocol
It uses the Routing tables in each node to store the next hop for the destination node
When choosing a discovery route from node A to node B, a broadcast is done from node A and if no direct route is found, the route is chosen by the intermediate nodes to reach node B.
Once the route is discovered till node B, the reply is sent through a unicast route discovered from node A to node B
Since broadcast is done from node A to node B multiple replies may be received by node A, it select the route with the best round trip time and use that route to node B for every next transmission
Trace Routing
While sending a unicast data with Trace Route enabled, each intermediate node send a route information packet (0x8D) back along the route to the originating node. This information packet contains:
Source and destination address of the unicast transmission
The address of the next hop in the route to the destination node
The address of the node generates the route information packet
Notes: Aggregate Route: Sometimes the data needs to be transmitted to a center aggregate node which a create an overhead in a DigiMesh network resulting in poor performance. To reduce this, use AG command to build an automatic route to the aggregate node.
Disable Routing: It shuts off the routing to reduce the network traffic.

## Slide 14: XBee & Arduino Communication
XBee-Arduino Library
  Download the XBee-Arduino Library either from manage libraries in the Arduino IDE or by going to https://github.com/andrewrapp/xbee-Arduino
  Among Series 1 and Series 2, we use Series 2 examples given after downloading this library. For working on XBee 900HP DigiMesh Module
TRANSMITTER
RECEIVER

## Slide 15: References
Datasheet of XBee 900HP DigiMesh Kit: https://www.digi.com/resources/documentation/digidocs/pdfs/90002173.pdf
01
GitHub page of Andrew Rapp: https://github.com/andrewrapp/xbee-Arduino
02
Building Wireless Sensor Network using Arduino – Dr. Matthijs Kooijman
03

## Slide 16: Questions?